## Slide 1
信號與系統
Signals & Systems
李琳山

## Slide 2
A Signal
A signal is a function of one or more variables, which conveys information on the nature of some physical phenomena.
Examples
    f ( t ) : a voice signal, a music signal
    f ( x , y ) : an image signal, a picture
    f ( x , y , t ) : a video signal
    xn : a sequence of data ( n: integer )
    bn : a bit stream ( b:1 or 0 )
    continuous-time, discrete-time
    analog, digital
  Human Perceptible/Machine Processed

## Slide 3
A Signal
: 1 1 0 1 0 1 0 0 1 0 1 0 0 1 …

## Slide 4
A System
An entity that manipulates one or more signals to accomplish some function, including yielding some new signals.
Examples
    an electric circuit
    a telephone handset
    a PC software receiving pictures from Internet
    a TV set
    a computer with some software handling some data
input
signal
System
output
signal

## Slide 5
Typical Examples of Signals/Systems
Concerned
Communication Systems
Transmitter
Receiver
Channel
Transmitted signal
noise, loss
distortion,
interference
Received signal
Estimate of message signal (information)
Message signal (information) data, text, audio, video
r(t)
s(t)

## Slide 6
Typical Examples of Signals/Systems
Concerned
Computers
Signal Processing Systems
    software systems processing the signal by computation/ memory
    examples : audio enhancement systems, picture processing systems, video compression systems, voice recognition/ synthesis systems, array signal processors, equalizers, etc.

## Slide 7
Audio Enhancement
Picture Processing

## Slide 8
Typical Examples of Signals/Systems
Concerned
Networks
user A
user B

## Slide 9
Typical Examples of Signals/Systems
Concerned
Information Retrieval Systems
The Global Internet
Other Information Systems
    examples : remote sensing systems, biomedical signal
    processing systems, etc.
Search Engine
Internet
User

## Slide 10
Global Internet
Digital
Libraries,
Virtual
Museums,
.
.
.
Electronic
Commerce,
Network
Banking,
.
.
.
Electronic
Government
Services,
.
.
.
Intelligent
Offices,
Distant
Learning,
.
.
.
Electronic
Home,
Network
Entertainment
.
.
.
Google,
Facebook,
YouTube,
Amazon
.
.
.
  The Global Internet

## Slide 11
  The Global Internet
Network Technology Connects Everywhere Globally
Huge Volume of Information Disseminated across the Globe in Microseconds
Multi-media, Multi-lingual, Multi-functionality
Cross-cultures, Cross-domains, Cross-regions
Integrating All Knowledge Systems and Information related Activities Globally

## Slide 12
  Typical Examples of Signals/Systems
  Concerned
Control Systems
    close-loop/feedback control systems
    example: aircraft landing systems, satellite stabilization systems, robot arm control systems, etc.
plant
controller
error signal e(t)
sensor
control signal v(t)
output signal y(t)
input signal x(t)
disturbance z(t)
feedback signal

## Slide 13
  Typical Examples of Signals/Systems
  Concerned
Other Systems
    manufacturing systems, computer-aided-design systems, mechanical systems, chemical process systems, etc.

## Slide 14
Scope of The Course
Those Signals/Systems Operated by Electricity, in Particular by Software and Computers, with Extensive Computation and Memory, for Information and Control Primarily
Analytical Framework to Handle Such Signals/Systems
Mathematical Description/Representation of Such Signals/Systems

## Slide 15
Scope of The Course
Language and Tools to Solve Problems with Such Signals/Systems
Closely Related to: Communications, Signal Processing, Computers, Networks, Control, Biomedical Engineering, Circuits, Chips, EM Waves, etc.
A Fundamental Course for E.E.

## Slide 16
Text/Reference Books and Lecture Notes
Textbook:
    Oppenheim & Willsky, “Signals & Systems”, 2nd Ed. 1997
    Prentice-Hall, 新月
Reference:
    S. Haykin & B.Van Veen, “Signals & Systems”, 1999
    John Willey & Sons, 歐亞
Lecture Notes:
    Available on web before the day of class

## Slide 17
Course Outline
    Fundamentals
    Linear Time-invariant Systems
    Fourier Series & Fourier Transform
    Discrete Fourier Transform (DFT)
    Time/Frequency Characterization of Signals/Systems
    Sampling & Sampling Theorem
    Communication Systems
    Laplace Transform
    Z-Transform
    Linear Feedback Systems
    Some Application Examples

## Slide 18
History of the Area
Independently Developed by People Working on Different Problems in Different Areas
Fast Development after Computers Become Available and Powerful
Re-organized into an Integrated Framework

## Slide 19
Background Required
2nd semester of 2nd year of EE
Mathematics
Pre-requisite : No
Grading
Midterm 40%
Final 40%
MATLAB Problems 20%

## Slide 20
每週準時上課認真聽講，不遲到缺席
每週自行閱讀課本，跟上上課進度
課本中上課未能提到之處，自行仔細研讀(含例題、習題)
學習要領
控制系統
訊號處理
網路導論
通訊原理
線性代數
微分方程
電路學
電子學

## Slide 21
1.0 Fundamentals
  1.1 Signals
    Continuous/Discrete-time Signals
      x(t), x[n]
    Signal Energy/Power

## Slide 22
Continuous/Discrete-time
x(t)
x[n]
n
t

## Slide 23
    Transformation of A Signal
      Time Shift
      Time Reversal
      Time Scaling
      Combination

## Slide 24
Time Scaling
x(t)
x(at), a<1
x(at), a>1
x[n]
?
?

## Slide 25
  Periodic Signal
    T0 : Fundamental period : the smallest positive value of T
    aperiodic : NOT periodic

## Slide 26
    Even/Odd Signals
      Even
      Odd
      Any signal can be discomposed into a sum of an
      even and an odd

## Slide 27
Even/Odd
Even
Odd
x(-t)=x(t)
x(-t)=-x(t)

## Slide 28
    Exponential/Sinusoidal Signals
  Basic Building Blocks from which one can construct many different signals and define frameworks for analyzing many different signals efficiently
fundamental period
fundamental frequency

## Slide 29
    Exponential/Sinusoidal Signals

## Slide 30
Vector Space
3-dim Vector Space

## Slide 31
N-dim Vector Space
(合成)
(分析)

## Slide 32
Signal Analysis

## Slide 33
  Exponential/Sinusoidal Signals
  Harmonically related signal sets
fundamental frequency
fundamental period
all with common period

## Slide 34
  Exponential/Sinusoidal Signals
  Sinusoidal signal
  General format
  Discrete-Time

## Slide 35
  Exponential/Sinusoidal Signals
  Important Differences Between Continuous-time and Discrete-time Exponential/Sinusoidal Signals
      For discrete-time, signals with frequencies ω0 and
      ω0 +m．2π are identical. This is Not true for
      continuous-time.
      see : Fig.1.27, p.27 of text

## Slide 36
Continuous/Discrete Sinusoidals

## Slide 38
Fig. 1.27
but
Note:

## Slide 39
  Exponential/Sinusoidal Signals
  Important Differences Between Continuous-time and Discrete-time Exponential/Sinusoidal Signals
      For discrete-time, ω0 is usually defined only for [-π, π] or [0, 2π]. For continuous-time, ω0 is defined for (-∞, ∞)
      For discrete-time, the signal is periodic only when
      ω0N=2πm,
      see : Fig.1.25, p.24 of text

## Slide 41
Harmonically Related Signal Sets

## Slide 42
  Exponential/Sinusoidal Signals
  Harmonically related discrete-time signal sets
  all with common period N
  This is different from continuous case. Only N distinct signals in this set.

## Slide 43
  Unit Impulse and Unit Step Functions
  Continuous-time
      First Derivative
      see: Fig1.33, Fig1.34, P,33 of text
      Running Integral
      Sampling property

## Slide 45
  Unit Impulse and Unit Step Functions
  Discrete-time
      First difference
      Running Sum
      Sampling property

## Slide 46
Unit Impulse & Unit Step
  Discrete-time
δ [n]
n
u [n]
n
n
u [n – 1]
δ [n] = u[n] – u[n – 1]

## Slide 47
Vector Space Representation of Discrete-
time Signals
  n-dim
)
)
0)
)
分析

## Slide 48
(⋯, 0, 0, 1, 0, 0, 0, ⋯ )=δ [ ]
(⋯, 0, 0, 0, 1, 0, 0, ⋯ )=δ [ – 1 ]
(⋯, 0, 0, 0, ⋯, 0, 1, ⋯ )=δ [ – k ]
分析
Vector Space Representation of Discrete-
time Signals
  n extended to

## Slide 49
  1.2 Systems
    Continuous/Discrete-time Systems
    Interconnections of Systems
        Series
        Parallel
x(t)
y(t)
x[n]
y[n]
+

## Slide 50
    Interconnections of Systems
        Feedback
        Combinations
+

## Slide 51
    Stability
        stable : bounded inputs lead to bounded outputs
    Time Invariance
        time invariant : behavior and characteristic of the system are fixed over time

## Slide 52
    Time Invariance
    Stability
Examples of unstable systems
x(t)
x(t-T0)
y(t)
y(t-T0)

## Slide 53
    Linearity
        linear : superposition property
        scaling or homogeneity property
        additive property

## Slide 54
    Memoryless/With Memory
        Memoryless : output at a given time depends only on the input at the same time
        eg.
        With Memory
        eg.

## Slide 55
    Invertibility
        invertible : distinct inputs lead to distinct outputs, i.e. an inverse system exits
        eg.
    Causality
        causal : output at any time depends on input at the same time and in the past
        eg.

## Slide 56
    Causality

## Slide 57
    Examples
Example 1.12, p.47 of text
Example 1.13, p.49 of text
“NOT” causal
causal
unstable
stable

## Slide 58
    Examples
Example 1.20, p.55 of text
zero input leads to zero output for linear systems
incrementally linear: difference between the responses to any two inputs is a linear function of the difference between the two inputs
“NOT” linear

## Slide 59
    Problem 1.35, p.64 of text
.
a has to divide N for N0 being an integer and N0 ≤ N
a has to divide k for m being an integer
a=gcd(k, N), N0 =N/gcd(k, N)
example: N=12, k=3, N0 =4, m=1
N=12, k=9, N0 =4, m=3
Selected problems for chap1: 4, 9, 14, 16, 18, 19, 27, 30, 35, 37, 47
fundamental period=?
,